## Slide 1
Vehicle Type and Speed Pattern Recognition

## Slide 2
Presentation Outline
1. Introduction and Problem Statement
2. Dataset and Preprocessing
3. Methodology and Architecture
4. Speed Estimation Algorithm
5. Results and Evaluation
6. Demo and Conclusions

## Slide 3
Problem Statement
THE CHALLENGE
Develop an automated system to detect vehicles, classify their type, and estimate their speed from traffic video footage.
KEY OBJECTIVES
Binary classification: Vehicle vs Non-vehicle
Multi-class: Car, Bus, Truck, Motorcycle
Speed estimation in mph from pixel motion
Real-time tracking with unique IDs
APPLICATIONS
Traffic Management
Law Enforcement
Road Safety
Urban Planning

## Slide 4
System Architecture
Video Input
→
MOG2 Detection
→
Centroid Tracker
→
CNN Classifier
→
Speed + Type
FRAMEWORKS
TensorFlow | Keras | OpenCV
TECHNIQUES
MOG2 | CNN | Centroid Tracking
OUTPUT
Annotated Video | CSV Data

## Slide 5
Datasets Used
Binary Detection
Vehicle Detection Image Set
Total: 17,760 images
Vehicles: 8,792
Non-vehicles: 8,968
Split: 80/20
Type Classification
Vehicle Detection 8 Classes
Total Patches: 19,700+
Classes Used: 4
Car, Bus, Truck, Motorcycle
Format: YOLO
Test Videos
Real Traffic Footage
M6 Motorway: 40s
Skybridge: 13s
Resolution: 720p/1080p
FPS: 30
Kaggle: Vehicle Detection Image Set (binary: vehicles vs non-vehicles).
Kaggle: Vehicle Detection 8 Classes (VOC boxes; we used a 4-class subset in the notebook).
Traffic video clips for end-to-end demo (detection → tracking → speed).

## Slide 6
CNN Architecture
INPUT 128x128x3
→
Conv 16
→
Conv 32
→
Conv 64
→
Conv 128
→
Dense 256
→
OUTPUT
Binary Model
Output: 1 neuron (Sigmoid)
Loss: Binary Cross entropy
Optimizer: Adam (1e-3)
99.2% Accuracy
Multi-Class Model
Output: 4 neurons (Softmax)
Loss: Categorical Cross entropy
Classes: Bus, Car, Motorcycle, Truck
94% Accuracy

## Slide 7
Vehicle Type Classification (Multi-class)
Predict vehicle type label (e.g., bus/car/truck/motorcycle).
We trained a lightweight CNN on labeled vehicle crops (subset used in notebook).
Notebook run achieved validation accuracy ≈ 95.9% after 5 epochs.
Goal
End-to-end overlay (type + speed + track ID)

## Slide 8
Vehicle Type Classification (Multi-class)
Foreground extraction: BackgroundSubtractorMOG2 (Gaussian mixture model).
Assign track IDs and keep per-track position history.
Tracking stability is critical before speed estimation.
Approach
Example overlay (IDs + pixel-domain speed)

## Slide 9
Vehicle Detection: MOG2
HOW MOG2 WORKS
1. Models each pixel as mixture of Gaussians
2. Learns background over time (history=500)
3. Identifies foreground (moving vehicles)
4. Shadow detection removed (gray=127)
POST-PROCESSING
Median blur (5x5) for noise removal
Binary threshold at 200
Morphological open/dilate
Contour detection (area greater than 900px)
Key Parameters
history = 500
varThreshold = 32
detectShadows = True
Detection Flow
Frame → ROI → FG Mask → Contours → BBoxes
Adaptive to lighting, handles multi-modal backgrounds, efficient for real-time

## Slide 10
Centroid Tracking Algorithm
ALGORITHM STEPS
1. Compute centroids from bounding boxes
2. Match detections to existing tracks
3. Update existing or create new IDs
4. Remove tracks after max_lost frames
Track Data Structure
centroid: (cx, cy)
bbox: (x, y, w, h)
lost: frame count
history: position list
KEY PARAMETERS
max_lost = 10 frames
dist_thresh = 60 pixels
History = Unlimited

## Slide 11
Speed Estimation Algorithm
STEP 1: PIXEL SPEED
dist_px = sqrt[(x2-x1)^2 + (y2-y1)^2]
time_s = window / fps
speed_pxps = dist_px / time_s
STEP 2: CALIBRATION
lane_px = 100 pixels (measured)
lane_meters = 3.65 m (standard)
meters_per_pixel = 0.0365
STEP 3: CONVERSION
speed_mps = speed_pxps * meters_per_pixel
speed_mph = speed_mps * 2.23694
COMPLETE FORMULA
V_mph = d_px * k * c / t
V = Speed (mph)
d = Pixel displacement
k = meters/pixel scale
c = 2.23694 conversion
Moving average (k=7) smoothing applied

## Slide 12
Speed Estimation
For each track: compute centroid displacement over a short window → px/s.
Convert px → meters using scene scale (lane width ≈ 3.65 m).
Convert m/s → mph (× 2.23694).
Computation
Scale example (two points define lane width in pixels)

## Slide 13
Stabilizing Speed: Smoothing / Filtering
Tracking noise creates spikes in instantaneous speed.
We applied a moving-average smoother (and explored Kalman-style filtering).
Smoother output is more stable for “speeding” decisions.
Why smoothing?

## Slide 14
Training Results
Binary Classification Model Performance
Training & Validation Curves
VALIDATION ACCURACY
99.2%
CLASSIFICATION REPORT
Precision
0.99
Recall
0.99
F1-Score
0.99
TRAINING DETAILS
Epochs Run
7 (Early Stop)
Best Epoch
5
Final Loss
0.024
Presenter: Member 1 (Ashwathi Ashok)

## Slide 15
Speed Estimation Results
M6 Motorway Video Analysis
Speed Over Time Chart
SPEED STATISTICS
Average Speed
45 mph
Max Speed
68 mph
Min Speed
22 mph
Std Deviation
±12 mph
TRACKING SUMMARY
Vehicles Tracked
50+
Frames Processed
1,200
Video Duration
~40 sec
Output: CSV file with frame-by-frame speed data for each tracked vehicle ID.

## Slide 16
Annotated Output
Real-Time Vehicle Detection, Classification & Speed Display
📦 Bounding Boxes
Color-coded by vehicle type with unique track IDs
🏷️ Labels
Vehicle type + real-time speed in mph
📊 CSV Export
Frame-by-frame tracking data for analysis
🎬 Video Output
MP4 with all annotations overlaid
Binary classifier (vehicle vs non-vehicle): ≈ 99.6% test accuracy.
Type classifier (bus/car/motorcycle/truck subset): ≈ 95.9% validation accuracy.
Speed estimation produces plausible mph trajectories; needs GT benchmark for MAE.

## Slide 17
Key Achievements
1
99.2% Detection Accuracy
Binary CNN classifier achieves near-perfect vehicle vs non-vehicle detection on validation set.
2
4-Class Type Classification
Successfully classifies vehicles into Car, Bus, Truck, and Motorcycle categories with 94% accuracy.
3
Real-Time Speed Estimation
Converts pixel motion to mph using lane-width calibration with smoothing for stability.
4
Robust Multi-Object Tracking
Centroid tracker maintains unique IDs across frames, handles occlusions gracefully.
5
End-to-End Pipeline
Complete system from raw video input to annotated output with CSV data export.
6
Multiple Video Sources
Tested on M6 Motorway and Skybridge videos demonstrating generalization.

## Slide 18
Challenges & Solutions
⚠️ CHALLENGE
Speed Estimation Noise
Frame-to-frame centroid jitter caused erratic speed readings
✓ SOLUTION
Moving Average Filter
Applied k=7 window smoothing and 5-frame displacement window
⚠️ CHALLENGE
Shadow Detection
MOG2 detected shadows as foreground objects
✓ SOLUTION
Shadow Removal
Set shadow pixels (gray=127) to 0 before thresholding
⚠️ CHALLENGE
Flickering Type Labels
Classification changed frame-to-frame for same vehicle
✓ SOLUTION
Majority Voting
Track votes per ID, display most common classification
⚠️ CHALLENGE
Camera Calibration
Unknown pixel-to-meter conversion factor
✓ SOLUTION
Lane Width Reference
Measured lane in pixels, used standard 3.65m width

## Slide 19
Future Work
Potential Improvements and Extensions
1
YOLO-based Detection
Replace MOG2 with YOLO v8 for more robust detection in varying conditions.
2
Homography Calibration
Implement camera calibration with homography matrix for accurate speed.
3
DeepSORT Tracking
Use deep appearance features to handle occlusions and re-identification.
4
Real-Time Optimization
GPU acceleration with TensorRT for edge deployment on NVIDIA Jetson.
5
Traffic Analytics
Add vehicle counting, lane occupancy, and congestion detection.
6
Night Vision Support
Train on infrared footage for 24/7 monitoring capability.

## Slide 20
Thank You!
PROJECT SUMMARY
We developed an end-to-end system for vehicle detection, type classification, and speed estimation using deep learning and computer vision techniques.
99%
Detection Acc.
94%
Classification
4
Vehicle Classes
Real
Time Speed